## Slide 1
Design of a Binary to Gray Code Converter Using Logisim
Digital Design and Computer Architecture (DDCA) — Project Presentation
Department : Freshman Engineering Department
Group : 6
KAKARAPARTI JOSHITHA SAI SAHASRA - 2620030378
PARUCHURI PRANAVI - 2620030409
KOMATIREDDY SAWNTHAN REDDY - 2620030437
MEREDDY SRI VARSHITH REDDY - 2620030438

## Slide 2
Introduction to Binary and Gray Code
Key Concepts
Binary Code
Represents numbers using only 0s and 1s.
Gray Code
A binary encoding where consecutive values differ by only one bit.
Advantage
Reduces ambiguity caused by multiple bits changing simultaneously.
Converter
Transforms a binary input into its corresponding Gray code output.
3-Bit Binary to Gray Code Comparison
Decimal | Binary | Gray Code
0 | 000 | 000
1 | 001 | 001
2 | 010 | 011
3 | 011 | 010
4 | 100 | 110
5 | 101 | 111

## Slide 3
Project Objectives and Logic Design
Objectives
1
Design a 4-bit binary-to-Gray code converter
2
Derive Boolean expressions
3
Implement using XOR gates in Logisim
4
Verify outputs using the truth table
Inputs & Outputs
Binary inputs: B3, B2, B1, B0 → Gray outputs: G3, G2, G1, G0
Boolean Expressions
G3 = B3
Direct pass-through
G2 = B3 ⊕ B2
XOR of B3 and B2
G1 = B2 ⊕ B1
XOR of B2 and B1
G0 = B1 ⊕ B0
XOR of B1 and B0
XOR outputs 1 when its two inputs are different.

## Slide 4
Truth Table of the 4-Bit Converter
Dec | B3 | B2 | B1 | B0 | G3 | G2 | G1 | G0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
5 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1
8 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
11 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
13 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1

## Slide 5
Circuit Implementation in Logisim
Circuit Architecture
The circuit is a combinational logic design requiring minimal components:
01
Direct Wire
B3 → G3: MSB is passed directly with no gate.
02
XOR Gate 1
B3 ⊕ B2 → G2
03
XOR Gate 2
B2 ⊕ B1 → G1
04
XOR Gate 3
B1 ⊕ B0 → G0
Three XOR gates and one direct connection are all that is needed for a complete 4-bit converter.

## Slide 6
Working of the Converter
Circuit Operation
G3 = B3
Directly copies the MSB.
G2 = B3 ⊕ B2
XOR of the two most significant bits.
G1 = B2 ⊕ B1
XOR of the middle two bits.
G0 = B1 ⊕ B0
XOR of the two least significant bits.
Worked Example
Binary input: 1011
B3 = 1, B2 = 0, B1 = 1, B0 = 1
Gray code output: 1 1 1 0
Verify by changing input switches in Logisim and comparing outputs against the truth table.
G3 = 1
Copy B3
G2 = 1⊕0 = 1
B3 XOR B2
G1 = 0⊕1 = 1
B2 XOR B1
G0 = 1⊕1 = 0
B1 XOR B0

## Slide 7
Applications and Conclusion
Real-World Applications
Rotary Encoders
Shaft and rotary position encoders in industrial machinery.
Position Measurement
Digital position measurement systems requiring error-free transitions.
Digital Electronics
Education and circuit simulation in digital design coursework.
Conclusion
A 4-bit binary-to-Gray converter is a combinational logic circuit.
Requires only one direct connection and three XOR gates.
Boolean expressions define the conversion mathematically.
The 16-row truth table verifies expected mapping for every input.
Logisim provides a convenient environment to implement and test the circuit.